Formal Methods of Validation

- Mathematically verifying the correctness of a software system
- A very attractive approach toward the correctness of computer-based control systems is that of model checking.
- Model checking is a formal verification technique which allows for desired behavioral properties of a given system to be verified on the basis of a suitable model of the system through systematic inspection of all states of the model.
- The system specification prescribes what the system should do and what not and thus constitutes the basis of verification process.
- DEFECT: If the system does not fulfill the specification.
- CORRECT: If the system satisfies the specifications
- We uses a verification technique called as model checking which is a software verification technique.
- Model-based verification techniques are based on models describing the possible system
  behavior in a mathematically precise and unambiguous manner.
- Models of the systems are expressed using finite state automata – finite set of states and set of transitions.
- To improve the quality of the model → simulation is done prior to verification→ which reduces the simpler errors before verification.
- Verification→ check whether we are building the things right.
- Validation→check whether the formal model is consistent with the informal conception of design.
- Transition systems: are basically directed graphs where nodes describes states and edges are transitions.
- S → S’ actions
- Labeled Transition system is a tuple of (S,S0,,A,→ )
- → = (S0, A, S)

UPPAAL

Click on the edge and then edit the properties
- Guard:The condition that must me satisfied to perfrom the operation.
- Update: What needs to be done after the action has taken place

Declarations: Do all the global declarations of he variables here.

system declarations: remove line 1&2 and the add the name of the new automata created in the 4th line system name1, name2,……

A[] not deadlock	deadlock

Automata_1.S3 -→Automata_1.S4	starvation
Automata_2.S3 -->Automata_2.S4

A[] not(Automata_1.S4 and Automata_2.S4) mutual exclusion